## Slide 1
Security Analysis of the Computer Architecture *OR* What a software researcher can teach you about *YOUR* computer
BSDaemon
Rodrigo Rubira Branco (BSDaemon)
rodrigo *noSPAM* kernelhacking.com
https://twitter.com/bsdaemon

## Slide 2: Disclaimers
I don’t speak for my employer. All the opinions and information here are of my responsibility (actually no one ever saw this talk before);
The talk focus mostly in Intel Skylake Architecture (Wikipedia says it will be released 2015-2016). I’ll try to generalize as much as I can though – in that, probably many mistakes might happen, so…
Interrupt me if you have questions or important comments at any point.
    IMPORTANT: No, I’m not part of the Intel Security Group (Mcafee)

## Slide 3: Start answering questions
I already anticipate a few questions:
  RNG -> I have no idea how strong it is, I believe it is not as strong as a specialized hardware but probably stronger than usual random generation mechanisms existent in the platform
  AMT -> I’ll talk a bit about the ME, but I’ll let the AMT research by Insinuator [0] to continue ;)
[0] http://www.insinuator.net/2014/03/how-to-use-intel-amt-and-have-some-fun-with-mainboards/

## Slide 4
Architecture The collection of features of a processor (or a system) as they are seen by the “user”
  User: a binary executable running on that processor, or
  assembly level programmer
μArchitecture The collection of features or way of implementation of a processor (or a system) that do not affect the user.
Features which change Timing/performance are considered microarchitecture.
Arch x uArch

## Slide 5
Architecture
  Registers data width (8/16/32/64)
  Instruction set
  Addressing modes
  Addressing methods (Segmentation, Paging, etc...)
  Protection
  etc…
mArchitecture
  Bus width
  Physical memory size
  Caches & Cache size
  Number of execution units
  Execution Pipelines, Number & type execution units
  Branch prediction
  TLB
  etc...
Timing is considered mArchitecture (though it is user visible!)
Arch and uArch elements

## Slide 6
System Agent
mouse
LAN
Lan
Adap
External Graphics
Card
South Bridge (PCH)
PCI express ×16
Audio Codec
DVD
Drive
Hard
Disk
Parallel Port
Serial Port
Floppy
Drive
PS/2 keybrd/ mouse
GFX
Cache
DDRIII
Channel 1
Mem BUS
DDRIII
Channel 2
Memory controller
Core
Core
D-sub, HDMI, DVI, Display port
Display link
2133-1066 MHz
Line in
Line out
S/PDIF in
S/PDIF out
Super I/O
LPC
USB
SATA
SATA
BIOS
PCI express ×1
exp
slots
4×DMI
Your computer

## Slide 7: Computer Complexity
IOMMU (Intel VT-d)
  What is it?
  How does it work -> Is it a chip or a software?
  Where is it located?

## Slide 8: Easy, another one…
How many processors your machine runs? (4? 8? 2 x 4 threads?)
Well…
  Your cpu’s (and threads)
  Your ME (Manageability Engine)
    INTERRUPT RECEIVED!!

## Slide 9: Interrupt Handler
DAL [1] (Dynamic Application Loader)
  Runs Java (permits 3rd part applications)
  ARC Processor
  Complete real-time OS
      IRET
[1] http://developers.txe.iil.intel.com/discover

## Slide 10: Processors…
PCU (Power Control Unit)
  Pure assembly OS (similar, but not fully compatible x86 ISA)
  Mainly comprises watchdogs for voltage failures (trying to recover or reset)
  Harvard Architecture (separate RAM/ROM)
PMC (Power Management Controller)
  Your PCH PCU
GPCU (Graphics PCU)

## Slide 11: Processors…
Your gigabit card
  Uops, research already done in that [2]
[2] http://www.alchemistowl.org/arrigo/Papers/Arrigo-Triulzi-PACSEC08-Project-Maux-II.pdf
VCU (Validation Control Unit)
BMC (servers)… [3]
[3] https://community.rapid7.com/community/metasploit/blog/2013/07/02/a-penetration-testers-guide-to-ipmi

## Slide 12: Tricky? Lets make it easier then…
How many execution modes your processor has?
  Real-mode?
  Virtual-8086 mode?
  Protected mode?
  SMM Mode? [4]
[4] My troopers talk and Phrack article on the subject
POC || GTFO 0x03
Net Watch: System Management Mode is not just for Governments

## Slide 13: Modes…
Where are the x64 folks?
  32e mode?
  64-bit mode?
  Those are more like ISA-related modes, similar to ARM Thumb I and/or II modes
More??
  VT-x anyone?
  SGX (Software Guard Extensions) anyone?
    More on this later

## Slide 14: Modes…
So, I’m bul*********?
  One is new (SGX is not even available yet) and the other is not exactly a mode…
What about cram mode then??
  Anyone? Note: CRAM != CAR (Yeap, I love Intel acronyms)

## Slide 15: Modes…
What about TXT? (GETSEC[SENTER]) to execute SINIT ACM -> AMD PRESIDIO?
  I’ll discuss this later as well ;)
  ACM (Authenticated Code Modules) run in CRAM mode
  Memory Areas protected by VT-d PMR or DPR (DMA Protected Region)
  Any code can be called and execute a MLE (Measured Launch Environment)
  BTW: Interesting ACM to have a look at: SCLEAN (clean system memory)
Probe mode anyone?
  For debugging with hardware debugger (ITP – In-Target Probe)
  Supports JTAG standard/protocol
  No regular instruction fetch (IP register not in use)
    PIR (Probe Mode Instruction Register)
    PDR (Probe Mode Data Register)
    Probe-mode special instructions
        PROBEMODE (to specify each core in PM or NOT)
        WRSUBPIR (to send instruction to CPU)
        READPDRT (read PDR)
    MSRs exclusive to probe mode (not real hardware register, only ucode functions)
        prob_lt_sp_cyc – Access LT private space
        prob_change_pg_bit – Disable/enable paging in 64 bit mode
  SMM special relation (Enter Probe mode thru Redirection)
        ICECTLPMR (redirection configuration bits) – MSR available in probe mode
        SMM_ENTER, SMM_EXIT, MC_ENTER, INIT, IR (interrupt)

## Slide 16
Yeap, life was easy… ;)

## Slide 17
Still missing a few we discussed

## Slide 18: Now it is very clear

## Slide 19: Software, software, software
That gets even better…:
  How much of your hardware is actually software?
    The ‘exported’ ISA is not exactly the same behind the wheels
    What about uCode patches? (who here don’t love cpu erratas?)
    Your ISA is translated to uCode, which has uInstructions that depend on the uArch (and parts of the process are bare metal)

## Slide 20: So, there are any backdoors?
Fair response (which I once heard but don’t remember the author to give the proper credits):
  None that I’m aware of (in my case I actually read the entire mov implementation)… but if you ask me again next Troopers (I’m sure you will not want to miss the next one after coming to this one, do you?) and I say I prefer to not comment, you might take your own conclusions ;)

## Slide 21: The feeling about security?

## Slide 22: TCB (Trusted Computing Base)
I don’t think considering vendor backdoors in Hardware by the big players should be in any TCB since:
  There are other (easier) ways to get access without involving a complex and difficult to hide and change hardware component
    Logistics interception
    Exploiting vulnerabilities (at this point I believe everyone agree that giving the complexity, the number of issues published is *SUPER* small – yeap, the teams at the companies are doing a good job, but still)

## Slide 23: What you can do to improve?
Work on validating your systems using FREE and WIDELY available technologies:
  TXT to get an image of what you have and compare with other companies that use different supply chains and are in different countries (this protects you against supply chain hijacks)
  Intel has a software called MtWilson that helps you do that (it also integrates with VM-based environments to collect data on kernel components of it) -> Honestly, I don’t even know what (if any) is the cost of it, but there are an open-source version (also made by Intel) [5]
  [5] https://github.com/OpenAttestation/

## Slide 24: Suggestion for a Project
Maybe a nice project to have is to share integrity values around the world, like nowadays people starting to share IOCs?
  Different BIOSes integrity values
  Different VMMs
This helps everyone finding already compromised systems, force the manufactures to publish such information and avoids supply chains hijacks ;)

## Slide 25: And what about the future?
Pointer Lookout
  SDE (Software Development Emulator) [6]
  Patch already available on GCC
[6] http://software.intel.com/en-us/articles/intel-software-development-emulator
SGX (Software Guard Extensions) [7] [8]
  Secure Enclaves
[7] http://software.intel.com/en-us/blogs/2013/09/26/protecting-application-secrets-with-intel-sgx
[8] https://sites.google.com/site/haspworkshop2013/workshop-program

## Slide 26
App
Malicious
App
OS
App
… and apps from each other …
X
OK
X
X
… UNTIL a malicious attacker gains full privileges and then tampers with the OS or other apps
Apps not protected from privileged code attacks
Attack
Bad
Code
Attack
SGX and what it tries to solve

## Slide 27: SGX details
Very different architecture (compared to ARM’s TrustZone):
  A Memory Encryption Engine (MEE) exists to encrypt memory data
  This protects a given memory region from hardware-based access
  Even with Intel privileged access, the keys are not exposed (they are erased if an unlock happens)
  OS is part of the TCB and thus seem as a malicious element

## Slide 28: SGX
Enclave
Enclave
Blob (dll)
Protected execution environment embedded in a process.
App Code
App Data
OS
Enclave Code
Enclave Data
With its own code and data
Provide Confidentiality
Provide Integrity
Controlled Entrypoints
With full access to app memory
TCS (*n)
Supports multi-threading
SECS

## Slide 29
SGX – Attack Surface
Proxy
Proxy
Proxy
Hardware
VMM
OS
App
App
App
X
X
Attack Surface today
X
Attack Surface with SE

## Slide 30: How SE Works: Protection vs. Software Attack
Untrusted Part of App
Trusted Part
of App
Create Enclave
CallTrusted Func.
Execute
Application
Other SW
Call Gate
App is built with trusted and untrusted parts
App runs & creates enclave which is placed in trusted memory
Trusted function is called; code running inside enclave sees data in clear; external access to data is denied
SSN: 999-84-2611

## Slide 31: How SE Works: Protection vs. Software Attack
Untrusted Part of App
Trusted Part
of App
Create Enclave
CallTrusted Func.
Execute
Return
(etc.)
Application
Other SW
Call Gate
App is built with trusted and untrusted parts
App runs & creates enclave which is placed in trusted memory
Trusted function is called; code running inside enclave sees data in clear; external access to data is denied
Function returns; enclave data remains in trusted memory
m8U3bcV#zP49Q

## Slide 32: SGX - MEE
Security perimeter is the CPU package boundary
Data and code unencrypted inside CPU package
Data and code outside CPU package is encrypted and integrity checked with replay protection
External memory reads and bus snoops see only encrypted data
Attempts to modify memory will be detected
Cores
Jco3lks937weu0cwejpoi9987v80we
Cache
System Memory
AMEX: 3234-134584-26864
CPU Package
Snoop
Snoop

## Slide 33
Virtual Address Space
ECREATE (Range)
Enclave
Code/Data
EADD (Copy Page)
Life Cycle of An Enclave
Before Entering
Enclave
Build
EINIT
Code/Data
Code/Data
Code/Data
Code/Data
Code/Data
Code/Data
EENTER
EEXIT
EREMOVE
ECREATE (Range)
EADD (Copy Page)
EINIT
EENTER
EEXIT
EREMOVE
EEXTEND
EEXTEND
Application is launched by OS
Application calls SE driver to allocate enclave
Driver calls ECREATE to allocate SECS
Application calls SE driver to add enclave pages to EPC
Driver calls EADD to add pages to EPC
Driver calls EEXTEND to extend measurement with initial contents of pages
Application calls SE driver to initialize enclave, providing SIGSTRUCT and LICTOKEN
Driver calls EINIT with SIGSTRUCT and LICTOKEN
Application enters enclave with EENTER
Enclave returns control to the application with EEXIT
Upon application exit, driver reclaims EPC pages with EREMOVE

## Slide 34: Example: Secure Transaction
Remote Platform
Client Application
Enclave
Authenticated Channel
Intel
Enclave built & measured against ISV’s signed manifest
Enclave requests REPORT from HW
REPORT & ephemeral key sent to server & verified
A trusted channel is established with remote server

1
2
3
4

## Slide 35: Example: Secure Transaction
Remote Platform
Client Application
Enclave
Authenticated Channel
Enclave built & measured against ISV’s signed manifest
Enclave requests REPORT from HW
REPORT & ephemeral key sent to server & verified
A trusted channel is established with remote server
A trusted channel is similarly established with secure input via the PSW enclave
User info sent securely to server
Application Key provisioned to enclave
Platform
SW
Enclave
Secure Input
ID
1
2
3
4
5
6
7

## Slide 36: Example: Secure Transaction
Remote Platform
Client Application
Enclave
Authenticated Channel
Enclave built & measured against ISV’s signed manifest
Enclave requests REPORT from HW
REPORT & ephemeral key sent to server & verified
A trusted channel is established with remote server
A trusted channel is similarly established with secure input via the PSW enclave
User info sent securely to server
Application Key provisioned to enclave
Enclave requests the HW Enclave-platform Sealing Key
Application Key encrypted using Sealing Key & stored for successive sessions
Platform
SW
Enclave
Secure Input
1
2
3
4
5
6
7
8
9

## Slide 37: SGX
EPC: Decrypted code and data space with
  SE access control
  Located in system memory space
  Implementation as stolen main memory (protected by MEE)
  Protected from SW by range registers
  Protected from HW by encryption and integrity protection
EPCM: Provide meta data for each EPC page
SE1 Instructions: 12 new operations
  ECREATE, EADD, EEXTEND, EINIT, EENTER, EIRET, EEXIT, EREMOVE, EDBGRD, EDBGWR, EREPORT, EGETKEY
2 Opcodes: 1 privileged; 1 unprivileged

## Slide 38: SGX Ring 0 Instructions
EAX | Leaf Function | Description
0x0 | ECREATE | Sets up the initial state environment, sets up the measurement, adds SECS page to EPC, measures attributes and xsave mask
0x1 | EADD | Adds a page to the enclave. Page can be used as enclave control, application data, code, stack, or heap
0x2 | EINIT | Verifies permit and marks the enclave ready to run
0x3 | EREMOVE | Removes pages from an enclave
0x4 | EDBGRD | Reads 8 bytes from a debug enclave
0x5 | EDBGWR | Writes 8 bytes to a debug enclave
0x6 | EEXTEND | Extends the measurement of the enclave with a measurement of an additional chunk of memory

## Slide 39: SGX Ring 3 Instructions
EAX | Leaf Function | Description
0x0 | EREPORT | Demonstrates cryptographically what was placed inside the enclave
0x1 | EGETKEY | Provides access to system secrets & user level keys
0x2 | EENTER | Transfers control to a predefined entry point within the enclave
0x3 | EIRET | Resume execution from its interrupt / exception point
0x4 | EEXIT | Returns from the enclave to the application

## Slide 40: BIOS, ACPI, others
Yes, huge code base!
Lots of OEM capabilities
Already been exploited by three letter agencies
  Chipsec: https://github.com/chipsec/chipsec
  Recently announced in CanSecWest (past week?)

## Slide 41
ISA Extensions?
AES-NI
AVX (SIMD)
Nice to discover huge NOPs in older systems:
66 66 0F 1F 84 00 00 00 00 00

## Slide 42: Conclusions
Folks, I could just keep going but I believe I made my points clear, but just to reinforce them:
  Your computer is actually a network of computers, running lots of software (Sergey Bratus and Langsec here at Troopers!)
  Modern architecture provides a way for you to generate a hardware attestation (TXT) and this is your way to protect against supply chain based attacks (sorry NSA, but I’m Brazilian)
  We need efforts on the community to use features that are already present and that solve many platform-related problems:
    Central base for sharing known good attestations?
    Software to manage and gather attestation information in networks, comparing to known good states and previously saved ones (OpenAttestation?)

## Slide 43
Thank You
BSDaemon
Rodrigo Rubira Branco (BSDaemon)
rodrigo *noSPAM* kernelhacking.com
https://twitter.com/bsdaemon